## Slide 1: Quantitative Characterization of Cellular Irregularities in Extruded Polystyrene Foam Using Digital Image Processing and Analysis
William A. Heeschen & Valentina Woodcraft
The Dow Chemical Company
Midland, Michigan
Motivation and Background
Image Analysis
Correlation of Human Rating with Image Analysis
Conclusions and Path Forward

## Slide 2: Motivation and Background
Flow - induced cell size irregularities in extruded foam structure  foam pattern
  Overall pattern strength
    Magnitude of difference between “small” and “large” cells
    Sharpness of boundaries between small-cell and large-cell domains
    Cell size consistency within domains
  Overall pattern shape due to extent of correlated sizes
Historic human panel rating is inconsistent.
Ubiquitous foam patterns + difficulty to quantify  need for robust analytical method
Minimal
Intermediate
Strong

## Slide 3: Image Analysis - Method
Ridge isolation: Remove Outliers… “bright” and “dark”
Find Ridges (Variance, Brightest, Darkest)
Pattern–based feature acceptance/rejection
Quantitative pattern assessment
  Line and Chevron count
  Summed line length
  Contrast-weighted line length (Ridge Factor)
Crop
Straighten
Center
Grayscale
Background
correct
Variance Filter
Find Ridges (Variance example)
Add All
Ridges
~10” x 24”

## Slide 4: Image Analysis – Detail of Keep/Reject Results
KEEPERS
Green/Variance
Cyan/Bright
Blue/Dark

## Slide 5: Image Analysis – Several Examples
KEEPERS
Green/Variance
Cyan/Bright
Blue/Dark
Line: |  | 27
Chev: |  | 8
Sum: |  | 4,257
Ridge: |  | 9,636
Line: |  | 116
Chev: |  | 29
Sum: |  | 30,642
Ridge: |  | 272,144
Line: |  | 10
Chev: |  | 15
Sum: |  | 2,969
Ridge: |  | 13,933
Line: |  | 87
Chev: |  | 15
Sum: |  | 17,179
Ridge: |  | 56,155

## Slide 6: Correlation of Human Rating with Image Analysis
Criteria (broad descriptions)
  Panelists ranked same images as image analysis algorithm
  Lowest rating (1) = least pattern features (lines, chevrons)
  Highest rating (10) = most pattern features
Averaged survey data compared to image analysis measures
Reasonable statistical correlation between human perception and image analysis data  model is useful!
Survey data
(9 panelists)
Image analysis data
(83 samples)
Correlation model
(JMP)

## Slide 7: Key ImageJ functions, plugins, etc.
Remove Outliers… (built-in)
  Bring locally-bright (dark) pixels in line with bulk in region
  Consolidate ridge (valley)
Variance… (built-in) to find “slopes” between ridges and valleys.
Find_Ridges (plugin by Bob Dougherty, OptiNav, Inc., http://www.optinav.com/imagej.html )
  Isolate gray-level ridges
  Applied to “bright”, “dark” and variance images
BinaryConnectivity to isolate nodes/trunks/branches in skeleton (from Gabriel Landini’s Morphology Package: http://www.mecourse.com/landinig/software/software.html )
ROI Manager (built-in) to manage feature boundaries

## Slide 8: Classifying Feature Outlines
Get XY coordinates of isolated-line skeletons (no nodes)
Find and assign ends, then eliminate the “other half” of the outline
“Line” vs “Chevron” from net curvature
Pointing direction (must point to center of pattern)
  Lines (slope/intercept passes through center)
  Chevron (use triangle to assess pointing direction)
    Base = two ends
    Vertex = point along curve at maximum distance from base
    “Orientation” is line from mid-point of base to vertex

## Slide 9: Conclusions and Path Forward
Current image analysis method generates reasonable agreement with panel results
Opportunities:
  Auto-center analysis region (special case for radial pattern)
  Better filtering for “crossing” ridges
  Adaptive recognition of chevrons

## Slide 10: Legal Disclaimer
Notice: No freedom from infringement of any patent owned by Dow or others is to be inferred. Because use conditions and applicable laws may differ from one location to another and may change with time, Customer is responsible for determining whether products and the information in this document are appropriate for Customer's use and for ensuring that Customer's workplace and disposal practices are in compliance with applicable laws and other government enactments. The product shown in this literature may not be available for sale and/or available in all geographies where Dow is represented. The claims made may not have been approved for use in all countries. Dow assumes no obligation or liability for the information in this document. References to “Dow” or the “Company” mean the Dow legal entity selling the products to Customer unless otherwise expressly noted. NO WARRANTIES ARE GIVEN; ALL IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR A PARTICULAR PURPOSE ARE EXPRESSLY EXCLUDED.

## Slide 11: End Of Talk